## Slide 1: Please delete this slide after reading through and before working on your slides
TIPS
Content provided in this lesson does not replace the i-STAT Alinity Quick Reference Guide, the i-STAT Alinity System Operations Manual, or the Instructions for Use (IFU) documents
This slide deck may be modified to represent products within the i-STAT Alinity System currently in use within your facility.
Once the deck has been modified, customers will assume responsibility for the content.*
Abbott will continue to provide and support the original resources that are made available on the www.globalpointofcare.abbott website.*
Not all products are available in all regions.
*Check the website regularly to ensure that you have the most up-to-date content.

## Slide 2: Troubleshooting
I-STAT ALINITY SYSTEM

## Slide 3: Learning Objectives
Define the term “Quality Check Failure”
Explain how to proceed on common troubleshooting issues when troubleshooting messages appear on the instrument’s screen
UNDERSTAND THE FOLLOWING:
Explain how to proceed when a Quality Check Failure Code appears on the instrument's screen

## Slide 4: Troubleshooting Overview
Cause
Resolution
i-STAT ALINITY QUALITY SYSTEM
Performs numerous quality checks during test cycle
Quality Check Failure (QCF)

## Slide 5
Troubleshooting Message
i-STAT ALINITY TROUBLESHOOTING
For in vitro diagnostic use only. For intended use and product details, visit www.globalpointofcare.abbott. Not all products are available in all regions. Check with your local representative for availability.
Photos & images are for illustrative purposes only. ©2025 Abbott. All rights reserved. i-STAT & Alinity are a trademarks of Abbott.| iLS Presentation i-STAT Alinity – Troubleshooting| APOC-25002814.2

## Slide 6: Low Battery
Resolution
Cause
Recharge the battery: Place the instrument with battery attached into the i-STAT Alinity Base Station
Make sure the Base Station has power
Refer to the System Operations Manual for additional troubleshooting messages
If the alert persists, contact the system administrator
BATTERY STATUS
CHARGE NEEDED SOON
CHARGE IMMEDIATELY
i-STAT ALINITY INSTRUMENT & BATTERY
i-STAT ALINITY BASE STATION
TROUBLESHOOTING MESSAGE

## Slide 7: Temperature Out of Range
Before performing testing, ensure that all equipment and materials are brought to room temperature within the range of 16°C to 30°C (61°F to 86°F) QCF codes shown in Review Results:
2-01-1.1.1
2-02-1.1.2
Resolution
Cause
TROUBLESHOOTING MESSAGE

## Slide 8
Quality Check Failure Codes
i-STAT ALINITY TROUBLESHOOTING
For in vitro diagnostic use only. For intended use and product details, visit www.globalpointofcare.abbott. Not all products are available in all regions. Check with your local representative for availability.
Photos & images are for illustrative purposes only. ©2025 Abbott. All rights reserved. i-STAT & Alinity are a trademarks of Abbott.| iLS Presentation i-STAT Alinity – Troubleshooting| APOC-25002814.2

## Slide 9: Overfill
QUALITY CHECK CODE FAILURE
Resolution
Cause

## Slide 10: Underfill
QUALITY CHECK CODE FAILURE
Resolution
Cause

## Slide 11
QUALITY CHECK CODE FAILURE
Resolution
Cause
Cartridge Handling

## Slide 12
QUALITY CHECK CODE FAILURE
Resolution
Cause
Sample Handling

## Slide 13: Resolve Quality Check Failures
Follow information presented on screen
Refer to i-STAT Alinity System Operations Manual
Contact your System Administrator

## Slide 14: Ensure Quality Sample
Failure to handle the cartridge properly may cause Quality Check Failures
MIX, MIX, MIX… Always mix properly and test promptly!
ENSURE A QUALITY SAMPLE IS OBTAINED:
Place instrument on a level, non-vibrating surface or in the base station during testing
Always correlate test results with the status of the patient

## Slide 15: Summary
NOW THAT YOU HAVE COMPLETED THIS LESSON, YOU SHOULD BE ABLE TO:
For more information refer to the i-STAT Alinity Getting Started Guides, System Operations Manual, and Quick Reference Guide.
Define the term “Quality Check Failure”
Explain how to proceed when Quality Check Code and Troubleshooting messages appear on the instrument’s screen

## Slide 16: Summary
Congratulations!
You have completed the lesson i-STAT Alinity – Troubleshooting